WH & NH COMPACT HOPPER RANGE

Warning: This product contains unprotected moving parts and is intended for inclusion within a host machine.  Manufacturers responsible for incorporating this Sub-assembly within a host machine must observe installation and safety instructions detailed in Section 2.10.

CONTENTS

Chapter                                                                                 Page Number

1.0	INTRODUCTION	4

1.1	Specific Features	4-5

2.0	OPERATION		6

2.1	Coin Size Range	6

2.2 	Dispensing Speed	6

2.3	Coin Capacity	7

2.4	Counting Method	7

2.5	Operating Temperature	7

2.6	Weight 		7

2.7	Installation	7

2.8	Accessories	7

2.9	Removing and Replacing the Hopper Bowl	8

2.9.1	WH-1	8

2.9.2	WH-3	8

2.9.3	WH-2 and NH-1	8

2.10	Safety and Maintenance	9-10

3.0	ELECTRICAL INFORMATION	11

3.1	Motor Voltage Option 	11

3.2	Current Consumption	11

3.3	Over Current Protection	11

3.4	Motor Power Connections	11

3.4.1	220v and 110v AC models	11

3.4.2	24v DC model	11

3.5	Proximity Sensor Features and Specifications	12

3.5.1	Features	12

3.5.2	Technical Specifications	12

3.6	Optical Sensor Type PS-50D-A	13

3.6.1	Specification	13

3.6.2	Connections	13

3.6.3	Operation	13

3.7	DC Motor Brake (DCMB) Specifications	14

3.8	Electro Magnetic Compatibility tests (EMC)	15

3.9	Instruction for Use	15

CONTENTS Continued

Chapter                                                                                 Page Number

4.0	DIMENSIONAL DRAWINGS	16

4.1	NH-1		16

4.2	WH-1		16

4.3	WH-2		17

4.4	WH-3		17

4.5	WH-2/U1	18

5.0	ASSEMBLY DRAWINGS & PARTS LISTS	19

5.1	NH-1

5.1.1	Assembly Drawing	20

5.1.2	Parts List	20

5.2	WH-1

5.2.1	Assembly Drawing	21

5.2.2	Parts List	22

5.3	WH-2

5.3.1	Assembly Drawing	23

5.3.2	Parts List	24,25

5.4	WH-3

5.4.1	Assembly Drawing	26

5.4.2	Parts List	27,28

5.5	WH-2/U1

5.5.1	Assembly Drawing	29

5.5.2	Parts List	30

1.0  INTRODUCTION

This family of compact hoppers includes the NH-1 and WH-1, WH-2 and WH-3  individual hoppers and the HM-3 and HM-4 hopper modules, all of which provide versatile solutions to medium-range coin dispensing requirements.

Fast coin dispensing is a feature of these hoppers and is achieved by using a powerful motor and a unique wiper mechanism.  Accuracy is achieved by use of a proximity sensor fitted as standard and activated by coins passing into the dispensing chute.

The hoppers are available in a range of sizes and coin disc options to suit cabinet space and coin type, with an escalator option available for the WH-2.

Hopper modules comprise of a number of individual hoppers mounted together  sharing a common dispensing chute.

The hopper bowl can easily be detached to facilitate cleaning and maintenance and the mechanism is mounted on a metal chassis to permit easy access to components.

All models are available with 115VAC, 220VAC or 24VDC motors which drive the dispensing mechanism via a gearbox, providing ample power.  Braking on the AC models is achieved mechanically on disconnection of power, by releasing a spring loaded latch which engages a notched plastic disc attached to the drive shaft.  An optional electronic motor brake is available on DC models.

1.1	Specific Features

1.1.1	WH-1

The WH-1 is 110mm wide and can dispense up to 600 coins per minute dependent upon coin diameter.  This hopper is provided with two opto sensors to prevent coin overrun.

1.1.2	WH-2

The WH-2 is 85mm wide and can hold up to 1000 coins.  This model is fitted with a release bar to simplify removal of the hopper head and can also be fitted with an extended hopper head which increases the capacity by up to 80%.

1.1.3	WH-3

The WH-3 is designed to hold very large coins or tokens (38mm diameter).  It has a capacity of 550 large coins and a dispensing speed of 310-900 coins per minute dependent upon coin diameter.

1.1.4	NH-1

The NH-1 hopper is 70mm wide making it the narrowest available.  In addition it has an interchangeable hopper bowl which enables easy access for servicing.  It handles smaller coins than the WH range and  can pay out up to 300 coins per minute.

An extended hopper head can be fitted which increases capacity by up to 80%.  An added feature of this model is a slide mounting which allows easy removal from the cabinet for refilling or servicing.

1.1.5	HM-3

The HM-3 is a hopper module which comprises three NH-1 compact hoppers all dispensing into a common chute.

1.1.6	HM-4

The HM-4 is a hopper module which comprises three NH-1 hoppers and one WH-2 hopper all dispensing into a common chute.

1.1.7	WH-2/U1

The WH-2/U1 is the only model in this range with an escalator which permits payout at a level higher than that of the hopper.

2.0  OPERATION

Coins are held in a detachable plastic hopper bowl immediately above the dispensing mechanism.  At the base of the hopper bowl is a circular metal disc mounted at 30( and driven by the motor via the gearbox.  Coins are collected in holes in a disc as it rotates in a counter clockwise direction.  As a coin approaches the payout point, it strikes a spring-loaded pin which deflects it towards the payout chute where it engages with the “wiper” ring.  This progresses the coin around in a clockwise direction against the coin guide.

Rotation of the wiper ring moves the coin towards the exit chute or escalator depending upon the model type.

A coin-counting facility is provided by provision of a proximity sensor mounted adjacent to the coin chute or at the top of the escalator.

2.1	Coin Size Range

| Model | Diameter | Thickness |
| --- | --- | --- |
| WH-1 | 19.0 - 28.5mm | 1.3 - 2.3mm |
| WH-2 | 19 – 25.5mm | 1.5 –3.2mm |
| WH-3 | 24.3 - 39.0mm | 1.6 - 3.3mm |
| NH-1 | 17.4 - 25.5mm | 1.1 - 3.2mm |
| WH-2/U1 | 21.0 - 25.5mm | 1.5 – 3.2mm |

2.2	Dispensing Speed (dependent upon coin diameter)

| Model | Speed (Approximate) |
| --- | --- |
| WH-1 | 600 coins/minute |
| WH-2 | 600 coins /minute |
| WH-3 | 900 coins /minute |
| NH-1 | 300 coins/minute |
| WH-2/U1 | 600 coins/minute |

2.3	Coin Capacity Examples

| Hopper Model | Coin Diameter |
| --- | --- |
|  | 22.5mm | 23.5mm | 24.5mm | 26.5mm | 30.8mm | 38.0mm |
| WH-1 | 1000 | 800 |  | 600 |  |  |
| WH-2 | 900 | 800 | 700 |  |  |  |
| WH-3 |  |  |  |  | 550 | 220 |
| NH-1 | 800 | 700 | 600 |  |  |  |
| WH-2/U1 | 900 | 800 | 700 |  |  |  |

2.4	Counting Method

All hoppers in this range are fitted with proximity sensors as standard.  The speed of dispensing prohibits the use of micro-switches.

2.5	Operating Temperature

All models in this range will operate within the range (10(C to +60(C.

2.6	Weight

| MODEL | WITH AC MOTOR | WITH DC MOTOR |
| --- | --- | --- |
| WH-1 | 3.7Kg | 2.6Kg |
| WH-2 | 3.7Kg | 2.1Kg |
| WH-3 | 3.8Kg | 2.6Kg |
| NH-1 | 2.9Kg | 2.1Kg |
| WH-2/U1 | 4.7Kg | 3.1Kg |
| HM-3 | 7.5Kg | 7.2Kg |
| HM-4 | 13.2Kg | 9.2Kg |

2.7	Installation

The base of the unit must be mounted to within 2( of the horizontal.  The slide mount supplied with the NH-1 may be detached for ease of mounting.

2.8	Accessories

A DC motor brake (DCMB-9101A) is available for all DC motors in this range.  (See Section 3.0 for technical specification).

Extended hopper heads are available for the NH-1 and WH-2 models.  High and low-level sensors are available for the WH range.

2.9	Hopper Bowl Removal and Replacement

2.9.1	WH-1

Remove the two M3 screws retaining the front of the bowl followed by the screw inside the bowl immediately behind the coin disc.  Replacement is a reversal of this procedure.

2.9.2	WH-3

Remove the two M3 screws retaining the front of the bowl before and lift clear of the chassis.  Replacement is a reversal of removal taking care to locate the rear of the bowl on the chassis lug before lowering the front into position.

2.9.3	WH-2 & NH-1

Removal is simplified on these models by the addition of a spring-loaded catch at the front of the bowl which should be pulled back before lifting the bowl free.

To replace, locate the rear of the bowl on the chassis lug extension before lowering the front into position and latching.

Picture of bowl removal

2.10	Safety and Maintenance

2.10.1	Control circuitry must be arranged to disconnect power to the mechanism when the host machine is opened for servicing.

The motors on AC models are wired to cater for 50Hz and 60Hz supplies by provision of two live connections (pink & blue).  Users must ensure that the unused wire is suitably terminated and insulated to avoid risk of electric shock as an electrical path exists between both connections.

2.10.2	Servicing and maintenance staff must be adequately trained and aware of the hazards presented by moving parts and high voltages.

Particular attention should be paid to the following areas:

- Motor connections and wiring (particularly 220V model).

- Coin disc (high torque created by drive through the gearbox).

- Cooling fan (metal blades rotating at high speed).

Fingers, long hair and loose clothing must be kept clear at all times when the mechanism is powered up.

2.10.3	Handle the mechanism with a firm grip on the frame as it is heavy.  Particularly avoid moving the mechanism when the bowl is full as injury or damage could result.

2.10.4	Avoid the inclusion of damaged coins and foreign objects such as matches, elastic bands, paper clips and screws during operation as these could cause jams.

2.10.5	Wiring errors or incorrect supply voltages can seriously damage the motor or sensors.  (See Section 3.0 for wiring details).

2.10.6	Routine maintenance should be undertaken every 2 months or after 50,000 coins have been dispensed, whichever is the sooner:

- Examine the wiring and sensor for damage.

- Check for loose screws and damaged components paying particular attention to the coin disc and wiper assembly.

- Clean the bowl with a damp cloth and detergent ensuring that it is fully dried.

- Dust should be brushed from the mechanism with a soft brush and if necessary dirt deposits can be removed with alcohol-impregnated wipes.

- Dust should be removed form the sensor with a small soft brush or low pressure air canister.

- Escalators, if fitted, should be cleaned with an alcohol-impregnated wipe paying particular attention to the ball in the non-return mechanism in the centre of the escalator.

3.0  ELECTRICAL INFORMATION

3.1	Motor Voltage Options

220VAC (with thermal protection)

110VAC

24VDC

3.2	Current Consumption (Peak)

| VOLTAGE | WH-1 | WH-2 | WH-3 | WH-2/U1 | NH-1 |
| --- | --- | --- | --- | --- | --- |
| 220VAC | 1.5A | 2.0A | 1.2A | 2.0A | 1.4A |
| 110VAC | 3.3A | 4.3A | 2.3A | 4.0A | 3.2A |
| 24VDC | 3.8A | 3.8A | 4.0A | 3.8A | 3.2A |

  - Over current protection

Customers control circuitry must be designed to ensure disconnection of the motor power supply within 5 seconds if a jam or stall situation occurs to prevent motor damage.

3.4	Motor Power Connections

3.4.1	220VAC and 110VAC Models

These models are supplied to cater for both 50 Hz and 60 Hz supplies and the wire colours are allocated as follows:

WHITE		COMMON

PINK			50Hz frequency

BLUE			60Hz frequency

N.B.	It is important to select the correct wire for the frequency of the supply and to insulate the unused one.  (Contact with the unused wire will give an electric shock or blow the supply fuse if earthed.)

The chassis of the coin hopper must be bonded to the supply earth and surrounding metal cabinet.

3.4.2	24VDC Model

This model is supplied with two wires, red and black.  To ensure correct directional rotation of the mechanism, the red wire must be connected +ve in relation to the black wire across a 24V ± 10% DC supply.

3.5	Proximity Sensor Features and Specifications

3.5.1	Features:

The sensor currently used on the compact hopper range is the AYS-02 which 	is a long life “non contact switch” with a quick response time and 40mA switching capabilities, making it suitable for direct interface with controllers.

3.5.2	Technical Specifications:

Detecting Distance:	4.5 (  0.5mm

Supply Voltage:	4.5V DC to 15VDC

Current Consumption:	10mA maximum at 15VDC

Response Frequency:	500Hz approximately

Output Logic:	Active High

Control Output:	40mA maximum (switching capability)

Residual Voltage:	1.0v maximum

Output Impedance:	4.7K(

Operating Temperature:	10(C to +60(C

Storage Temperature:	(20(C to +85(C

Figure 3.5.2 (Sensor Circuit)

#### 3.6	Optical Sensor Type PS - 50D-A(Used on dual exit escalators only)

3.6.1	Specification

| Description | Signal | Min | Ave | Max | Unit | Conditions |
| --- | --- | --- | --- | --- | --- | --- |
| Operating Voltage | Voc | 4.75 |  | 5.25 | V |  |
| Low level O/P | Vol |  |  | 0.4 | V | Voc=5v, Iol=10mA |
| High level O/P | Voh | 4.0 |  |  | V | Vcc=5V,RL=1K( |
| Low level current | IccL |  | 16 | 25 | mA | Vcc=5 |
| High level current | IccH |  | 17 | 40 | mA | Voc=5 |
| Short det. distance | LDS |  |  | 2 | mm | Vcc=5V,RL=1K( |
| Long det. distance | LDL | 6 |  |  | mm | (90% beam broken) |
| Interference range | LNS |  |  | 25 | mm |  |
| Reaction | L to H | tPLH |  |  | 0.5 | ms | Voc=5V, RL=1K( |
| Time | H to L | tPHL |  |  | 0.5 | ms |  |
| Light Intensity | Ev | 8000 |  |  | LX | Vcc=5V,RL=1K( |

3.6.2	Connections

### 3.6.3	Operation

Connect a suitable resistor between the supply and signal leads and ensure a supply voltage of  5 Volts DC ± 0.25Volts.

When no coin is present the signal lead potential tends towards 0 Volts.

When a coin passes the lenses the 5 Volt supply voltage will be seen on the signal lead giving an active high output.

3.7	DC Motor Brake (DCMB) Specification

The DCMB-9101A is a brake circuit board which stops DC motors quickly by applying a short circuit.  Electrical connection is by two AMP E1 series connectors.

| Connector | Pin | Signal Name | Signal Type | Detail |
| --- | --- | --- | --- | --- |
| J1 | 1 | Motor On (ve | Input | Connect to 0V |
| J1 | 2 | Motor On +ve | Input | Pull up 5V – 12V |
| J1 | 3 | 0V | Supply | Connect to 0V |
| J1 | 4 | 24V DC | Supply | Connect to 24V DC* |
| J2 | 1 | Motor ( | Output | Connect to motor |
| J2 | 2 | Motor + | Output | Connect to motor** |

Table 3.7 (Wiring details)

*	The unit draws 2 – 5mA when idle and 300mA(max) when driving the motor.

**	Drive capability: 5A (max).

Figure 3.7.1 (Motor brake circuit)

Fig. 3.7.2 – Picture of DCMB motor brake

3.8	EMC Testing

European Directive for Electro-Magnetic Compatibility (EMC) 89/336/EEC.

Our interpretation of the EMC directive is that our products are not intended to	be “placed on the market as a single commercial unit for final use”, and the only mandatory provision is to include instructions for use.

3.9	Instructions for Use

These products can present potentially serious hazards to users if adequate precautions are not taken.

Refer to safety and maintenance in Section 2.10 for detailed precautions to be followed  by manufacturers and users.

4.0  DIMENSIONAL DRAWINGS

4.1	NH-1

4.2	WH-1

4.3	WH-2

4.4	WH-3

4.5	WH-2/U1

5.0  PARTS LISTS

5.1	NH-1 (24vdc)

5.1.1	Exploded Drawing

5.1.2		NH-1 Parts List (24V Motor version)

| No. | Part Name | No. | Part Name |
| --- | --- | --- | --- |
| 1 | Lower Chassis | 41 | Joint Spring |
| 2 | Screw M3 x 5 | 42 | Agitating Shaft |
| 3 | Upper Chassis | 43 | Screw M4 x 10 |
| 4 | Body Fixing Plate | 44 | Hood |
| 5 | Screw M3 x 6 | 45 | Agitation Spring |
| 6 | Chassis Stopper | 46 | Agitating Boss |
| 7 | Screw M3 x 8 | 47 | Spring Pin |
| 8 | Chassis Fixing Shaft | 48 | Disc Collar |
| 9 | Screw M3 x 8 | 49 | Disc |
| 10 | Chassis (R) | 50 | Agitating Rubber |
| 11 | Screw M3 X 4 | 51 | Twisted Coil Spring |
| 12 | Chute Plate | 52 | Chute Pin |
| 13 | Motor | 53 | Sub Wiper Assy |
| 14 | Washer 4 x 15 x1 | 54 | Compressed Spring |
| 15 | Head Latch Shaft | 55 | Washer 4x8x0.5 |
| 16 | Head Latch | 56 | Nut M3.5 |
| 17 | Head Latch Spring | 57 | Hexagon Bolt M4x4 |
| 18 | Bolt M4 x 6 SW | 58 | Hood Guide |
| 19 | Washer 4 x 10 x 1.4 | 59 | Head |
| 20 | Coin Regulating Plate | 60 | #4 E Ring |
| 21 | Coin Regulating Leaf Spring Assy | 61 | Head Shaft |
| 22 | Screw M4 x 10 | 62 | Agitator Clamp |
| 23 | Screw M4 x 6 | 63 | Agitating Rubber |
| 24 | Coin Supporting Plate | 64 | DC Motor Brake (Accessory) |
| 25 | Guide Frame | 65 | Connector (from motor) |
| 26 | Screw M4 x 8 | 66 | Connector (supply & control) |
| 27 | Sensor | 67 | Screw M3 x 6 CSK |
| 28 | Screw M2.6 x 12 | 68 | Chassis (L) |
| 29 | Roller | 69 | Washer 3 x 6 x 0.3 |
| 30 | Actuator Ass’y |  |  |
| 31 | #2 E Ring |  |  |
| 32 | Washer 3 x 6 x 0.5 |  |  |
| 33 | Screw M2.6 x 3 |  |  |
| 34 | Actuator Spring |  |  |
| 35 | Screw M3 x 8 |  |  |
| 36 | Base |  |  |
| 37 | Polyslider 4 x 12 x 0.25 |  |  |
| 38 | Wiper Collar |  |  |
| 39 | Wiper Ring |  |  |
| 40 | Agitating Collar |  |  |

5.2	WH-1 (AC Model)

5.2.1	Exploded Drawing

5.2.2	WH-1 Parts List

| No. | Part Name | No. | Part Name |
| --- | --- | --- | --- |
| 1 | Hopper Head | 41 | Screw M3 x 8 |
| 2 | Rubber Cushion | 42 | Screw M4 x 6 |
| 3 | Screw M3x10 | 43 | Guide Plate |
| 4 | Nut M5 | 44 | Screw M4 x 6 |
| 5 | Sub Wiper Spring | 45 | Chute Box |
| 6 | Sub Wiper Bracket | 46 | Chute Plate |
| 7 | Sub Wiper | 47 | Screw M3 x 5 |
| 8 | Chute Boss | 48 | Joint Collar |
| 9 | Coil Spring | 49 | Screw M4 x 6 (W point) |
| 10 | Hood Guide | 50 | Motor Ass’y |
| 11 | Polyslider washer 0.25T | 51 | Motor cooling fan |
| 12 | Screw M3x10 | 52 | Hexagon bolt M4 x 4 |
| 13 | Wiper Stopper | 53 | Ball Bearing 11mm |
| 14 | Screw M4 x 8 | 54 | Screw M4 x 4 |
| 15 | Main Chassis | 55 | Coin regulating leaf spring |
| 16 | Chassis Side Plate (L) | 56 | Roller |
| 17 | Chassis Side Plate (R) | 57 | Coin Regulating Assy. |
| 18 | Bottom Chassis | 58 | Screw M2.6 x 15 |
| 19 | Nut M5 | 59 | 2mm E ring |
| 20 | Screw M4 x 10 | 60 | Actuator Assy. |
| 21 | Washer 4 x 10 x 1.4 | 61 | Sub Actuator Assy |
| 22 | Sub Hood | 62 | Actuator Spring |
| 23 | Hood | 63 | Guide Lever |
| 24 | Disc | 64 | Lever Bracket |
| 25 | Polyslider Washer 0.25T | 65 | Washer M3 x 4 |
| 26 | Screw M4 x 6 | 66 | Wiper Stopper Plate |
| 27 | Screw M4 x 8 | 67 | Nut M3 |
| 28 | Proximity Sensor | 68 | Ball Retaining spring (Long) |
| 29 | Screw M3 x 4 | 69 | Ball Retaining spring (Short) |
| 30 | Screw M3 x 8 |  |  |
| 31 | Wiper Plate |  |  |
| 32 | Sensor Bracket |  |  |
| 33 | Screw M3 x 3 |  |  |
| 34 | Nut Plate |  |  |
| 35 | Sensor Cove |  |  |
| 36 | Screw M4 x 6 |  |  |
| 37 | Sub sensor bracket |  |  |
| 38 | Sub bracket |  |  |
| 39 | Plastic Cover |  |  |
| 40 | Screw M4 x 15 |  |  |

5.3	WH-2 (AC Model)

5.3.1	Exploded Drawing

5.3.2	WH-2 Parts List

| No. | Part name | Part no |
| --- | --- | --- |
| 1 | Bottom Chassis | TDA-3025 |
| 2 | Screw M4 x 8 | 80S-WS10-0-15 |
| 3 | Chassis (R) AC motor | TDA-3053 |
| 3 | Chassis (R) DC motor | TDA-3034 |
| 4 | Chassis (L) AC motor | TDA-3054 |
| 4 | Chassis (L) DC motor | TDA-3035 |
| 5 | Motor Cooling Fan |  |
| 6 | Fan Holding Screw |  |
| 7 | AC motor assy |  |
| 7 | DC(24V) motor/gearbox | ZAA-1507-A-10 |
| 7 | DC(24V) motor | ZAA-1507-A |
| 8 | Screw M4 x 4 | 80S-RH10-0-64 |
| 9 | Washer 4 x 10 x 1.0 | 80W-F101-0-41 |
| 10 | Regulator Spring assy |  |
| 11 | Regulator Collar | NEW-3079 |
| 12 | Wiper Boss | TDA-3018 |
| 13 | Hexagon Bolt M4 x 6 | 80S-ST10-0-36 |
| 14 | Chute | TDA-3008 |
| 15 | Screw M3 x 8 | 80S-WS10-0-06 |
| 16 | Guide Plate 2.0T | TDA-3010 |
| 16 | Guide Plate 2.6T | TDA-3098 |
| 16 | Guide Plate 3.2T | TDA-3099 |
| 17 | Screw M4 x 8 | 80S-WS10-0-33 |
| 18 | Actuator assy | TDA-2038 |
| 19 | Screw M3 x 4 | 80S-RS10-0-06 |
| 20 | Screw M3 x 4 | 80S-LS10-0-07 |
| 21 | Screw M2.6 x 4 | 80S-LS10-0-01 |
| 22 | Sensor Bracket | TDA-3033 |
| 23 | Sensor (AYS-02) | ZDS-3050 |
| 23 | Sensor (CS-A5) | ZDS-3100 |
| 24 | Sensor Cover | TDA-3015 |
| 25 | Screw M3 x 6 | 80S-WS10-0-05 |
| 26 | Chute Bracket | TDA-3009 |
| 27 | Wiper Polyslider 0.13mm | NFW-3041 |
| 27 | Wiper Polyslider 0.25mm | NFW-3042 |
| 28 | Wiper |  |
| 29 | Bolt M3 x 8 | 80B-CB00-0-02 |
| 30 | Agitating bar | TDA-2029 |
| 31 | Joint Spring |  |
| 32 | Agitator Bar |  |
| 33 | Plastic Cover | TDA-3027 |
| 34 | Screw M4 x 10 | 80S-WS10-0-16 |
| No | Part name | Part No |
| 35 | Screw M3 x 25 | 80S-RH10-0-52 |
| 36 | Nut M4 (S) | 80N-HN10-0-21 |
| 37 | Sub Wiper Spring | TDA-3024 |
| 38 | Nut M4 (L) | 80N-HN10-0-21 |
| 39 | Screw M4 x 6 | 80S-CS10-0-22 |
| 40 | Hood | TDA-3003 |
| 41 | Disc 20mm 1.5mm gap | TDA-3036 |
| 41 | Disc 22mm 1.95mm gap | TDA-3026 |
| 41 | Disc 22mm 1.65mm gap | TDA-3163 |
| 41 | Disc 22mm 1.6mm gap | TDA-3144 |
| 41 | Disc 24mm 1.7mm gap | TDA-3029 |
| 41 | Disc 26mm 1.8mm gap | TDA-3001 |
| 41 | Disc 26mm 1.5mm gap | TDA-3123 |
| 41 | Disc 27.5mm 1.8 mm gap | TDA-3019 |
| 41 | Disc 27.5mm 1.6mm gap | TDA-3065 |
| 42 | Disc Polyslider 0.13mm | TDA-3048 |
| 42 | Disc Polyslider 0.25mm | TDA-3022 |
| 42 | Disc Polyslider 0.5mm | TDA-3031 |
| 43 | Base |  |
| 44 | Head Shaft | TBN-3036 |
| 45 | Head Fixing Spring | TBN-3037 |
| 46 | Head Release Bar | DNH-3001 |
| 47 | E ring 2mm | 80R-ER10-0-03 |
| 48 | Screw M4 x 8 | 80S-CS10-0-23 |
| 49 | Hood Guide |  |
| 50 | Washer 4 x 10 x 1.0 | 80W-FW01-0-41 |
| 51 | Taper Spring | AHC-3042 |
| 52 | Chute Pin | TDA-3020 |
| 53 | Chute Boss | TDA-3021 |
| 54 | Screw M2.6 x 3 | 80S-RH00-0-13 |
| 55 | Sub Wiper | TDA-3016 |
| 56 | Sub Wiper Bracket |  |
| 57 | Hopper Head |  |
| 58 | E ring 4mm | 80R-ER10-0-07 |
| 59 | Hopper head fixing shaft | TBN-3038 |

5.4	WH-3 (AC Model)

5.4.1	Exploded Drawing

5.4.2	WH-3 Parts List

| No | Part name | Part no |
| --- | --- | --- |
| 1 | Hopper Head | TEA-3038-A |
| 2 | Screw M3 x 10 | 80S-LS10-0-12 |
| 3 | Motor AC P540A-241 (115V) | ZAA-2015-A |
| 3 | Motor AC P540A-242 (115V) | ZAA-2016-A |
| 3 | Motor AC P540A-252 (220V) | ZAA-2022-A |
| 4 | Base | TEA-3004-B |
| 5 | Screw M4 x 6 | 80S-CS10-0-22 |
| 6 | Screw M4 x 8 | 80S-CS10-0-23 |
| 7 | Hood Guide 1.6t | TEA-3008-B |
| 7 | Hood Guide 2.0t | TEA-3008-B-10 |
| 7 | Hood Guide 1.4t | TEA-3008-B-20 |
| 7 | Hood Guide 1.8t | TEA-3008-B-30 |
| 7 | Hood Guide 2.6t | TEA-3008-B-40 |
| 7 | Hood Guide 2.9t | TEA-3118-A |
| 8 | Hood | TEA-3003-D |
| 9 | Screw M4 x 10 | 80S-WS10-0-16 |
| 10 | Hexagon Bolt M4 x 6 | 80S-ST10-0-36 |
| 11 | Disc 40mm | TEA-3001-B |
| 11 | Disc 32mm | TEA-3010-C |
| 11 | Disc 26mm | TEA-3027-C |
| 12 | Nut M4 | 80N-HN10-0-25 |
| 13 | Nut M4(S) |  |
| 14 | Chute Pin | TEA-3026-A |
| 15 | Sub Wiper Bracket 2.0t | TEA-3013-A |
| 15 | Sub Wiper Bracket 1.6t | TEA-3013-A-10 |
| 15 | Sub Wiper Bracket 1.8t | TEA-3013-A-20 |
| 15 | Sub Wiper Bracket 2.3t | TEA-3104-A |
| 15 | Sub Wiper Bracket 2.5t | TEA-3105-A |
| 15 | Sub Wiper Bracket 2.9t | TEA-3119-A |
| 16 | Sub Wiper 32-40mm | TEA-3012-B |
| 16 | Sub Wiper 26-28mm | TEA-3033-0 |
| 16 | Sub Wiper 30.8mm | TEA-3047-0 |
| 17 | Wiper Boss | NFW-3026-A |
| 18 | Taper Spring | AHC-3042-0 |
| 19 | Screw M2.6 x 3 | 80S-CS10-0-35 |
| 20 | Screw M3 x 6 | 80S-WS10-0-05 |
| 21 | Chute | TEA-3011-B |
| 22 | Coin Regulating Plate 4.8mm | TEA-2002-0 |
| 22 | Coin Regulating Plate 5.0mm | TEA-2003-0 |
| 22 | Coin Regulating Plate 5.2mm | TEA-2004-0 |
| 22 | Coin Regulating Plate 5.5mm | TEA-2005-0 |
| 22 | Coin Regulating Plate 4.6mm | TEA-4006-0 |
| 22 | Coin Regulating Plate 4.3mm | TEA-2007-0 |
| 23 | Coin Regulating Leaf Spring | TEA-3014-A |
| 24 | Washer 4 x 10 x 1.4 | 80W-FW00-0-62 |
| 25 | Bolt M4 x 6 | 80B-PH10-002 |
| 26 | Screw M4 x 8 | 80S-WS10-0-15 |
| 27 | Bottom Chassis | TEA-3007-B |
| 28 | Chassis (R) AC motor | TEA-3005-A |
| 29 | Chassis (L) AC motor | TEA-3006-A |
| 30 | Guide Plate 2.5t | TEA-3009-A |
| 30 | Guide Plate 3.2t | TEA-3009-A-10 |
| 30 | Guide Plate 2.0t | TEA-3009-A-20 |
| 31 | Sensor Cover | TEA-3015-D |
| 32 | Proximity Sensor AYS-02 | ZDS-3050-0 |
| 32 | Proximity Sensor CS-A5 | ZDS-3100-A |
| 33 | Screw M3 x 3 | 80S-WS10-0-04 |
| 34 | Screw M3 x 8 | 80S-RH10-0-40 |
| 35 | Plastic Cover | TEA-3019-0 |
| 36 | Screw M3 x 15 | 80S-RH10-0-46 |
| 37 | Screw M2.6 x 4 | 80S-LS10-0-01 |
| 38 | Sensor Bracket | TDA-3033-0 |
| 39 | Screw M3 x 4 | 80S-RS10-0-06 |
| 40 | Actuator assy | NFW-2009-0 |
| 40 | Actuator assy | NFW-3031-0 |
| 40 | Actuator assy | TDA-3039-0 |
| 41 | Screw M3x8 | 80B-CB10-0-02 |
| 42 | Wiper (3 hole disc) | TEA-3016-B |
| 42 | Wiper (4 hole disc) | TEA-3028-0 |
| 42 | Wiper (5 hole disc) | TEA-3083-0 |
| 43 | Wiper Boss | TEA-3017-0 |
| 44 | Screw M3 x 8 | 80S-WS10-0-24 |
| 45 | Stirring Rubber | TEA-3086-0 |
| 46 | Stirring Rubber Retainer | NFW-3093-0 |
| 47 | Motor/gearbox 24V DC 60RPM | ZAA-1601-A |
| 47 | Motor/gearbox 24V DC 110RPM | ZAA1603-A |
| 48 | Chassis (R) for DC Motor | TEA-3021-A |
| 49 | Chassis (L) for DC Motor | TEA-3022-A |
| 50 | Rubber Washer | IAD-3046-A |
| 51 | Screw M3 x 8 | 80S-CS10-0-17 |
| 52 | Washer 4 x 15 x 1mm | 80W-FW00-0-67 |
| 53 | M3 Spring Washer | 80W-SW10-0-07 |
| 54 | M3 Nut | 80N-HN10-0-09 |
| 55 | Coin Head Plate | TEA-3037-A |

5.5	WH-2/U1

5.5.1	Exploded Drawing

5.5.2	WH-2/U1 Parts List (See non escalator option for common parts)

| 1. | Base | 21 | Sub-bracket assembly |
| --- | --- | --- | --- |
| 2. | Guide rail assembly | 22 | Sensor bracket |
| 3. | Coin cover | 23 | Nut M2.6 x 12 |
| 4. | Screw M3 x 8 | 24 | Proximity sensor |
| 5 | Polyslider 0.25t | 25 | Screw M3 x 4 |
| 6 | Roller spring | 26 | Actuator spring |
| 7 | Roller Shaft | 27 | E ring 2mm |
| 8 | Polyslider 0.13t | 28 | Actuator assembly |
| 9 | Coin roller | 29 | Roller |
| 10 | Spring collar | 30 | Self-lubricating roller |
| 11 | E ring 3mm | 31 | Escalator support bracket |
| 12 | Cover | 32 | Screw M4 x 6 |
| 13 | Screw M4 x 10 | 33 | Coin guide cover |
| 14 | Top cover | 34 | Screw M4 x 15 |
| 15 | Screw M3 x 10 | 35 | Coin Guide (L) |
| 16 | Inner guide | 36 | Coin Guide (R) |
| 17 | Top right guide | 37 | Flat Washer M5 x 10 x 0.5 |
| 18 | Edge plate | 38 | Nut M3 x 3 |
| 19 | Spacer | 39 | Screw M3 x 10 |
| 20 | Back plate |  |  |

6.0	DOCUMENT CONTROL

| Date | Issue No. | Reason for Revision | Page No. |
| --- | --- | --- | --- |
| 1/09/98 | Compact Hopper-Draft |  |  |
| 23/02/99 | Compact Hopper-Iss. 1 | Dimensions & parts list added |  |
| 08/02/02 | Compact Hopper-Iss. 2 | Optical sensor specification Over current protection Text changes | 13 11 Various |
| 18/04/06 | Compact Hopper iss 3 | Coin ranges reviewed | Various |
| 05/09/06 | Compact hopper iss 4 | Coin ranges reviewed | Various |
| 05/09/06 | Compact hoppers iss 5 | Part no’s added ASI issue. | 24,25,27,28. |

# Text boxes

DCMB - 9101A

1

2

(Black)

(Red)

J2

J1

470(

300 mA max)

2

3

1

4

(Black)

ON – (Green)

ON+ (Orange)

+ 24v (red)

GND (Black)

0VVV

Proximity switch

main circuit

4.7K(

M

SIGNAL

(White)

VCC

(Red)

VCC (Red)

Signal (White)

Ground (Black)

Lenses

Pull-up resistor